## Slide 1
ESP8266
Buttons
TTL
Home Assistant
ESPHOME
API
Barcode Scanner
Serial TTL
Voice Assistant
TTS
Thermal Printer
Serial TTL
Mobile Phone
HA Client
Display
I2C
Touchscreen
HA Client
Home Assistant Shopping list

## Slide 2
ESP8266
Buttons
TTL
Home Assistant
ESPHOME
API
Barcode Scanner
Serial TTL
Voice Assistant
TTS
Thermal Printer
Serial TTL
Mobile Phone
HA Client
Display
I2C
Touchscreen
HA Client
Mealie Integration
Mealie
MEALIE Shopping list

## Slide 3
GPIO14
Gnd
Gnd
5V
Buzzer
Power
Gnd
GPIO01
Gnd
GPIO00
Gnd
GPIO03
Gnd
GPIO16
Button Left
Button Right
GPIO04
GPIO05
3v3
Gnd
GPIO13
GPIO15
Gnd
3v3
I2C Display
Scanner
SW
sda
SW
LED
scl
Rx
Tx
GM60

## Slide 4
 | TOUT |  |  |  |  | GPIO16 | BUTTON – LED - ROOD
LEDs & BUTTONS - GND | GND |  |  |  |  | GPIO05 | DISPLAY – SCL – GROEN
 | Vout USB |  |  |  |  | GPIO04 | DISPLAY – SDA – BLAUW
 | GPIO10 | ESP8266 |  |  |  | GPIO00 | BUTTON – LED - ROOD
 | GPIO09 |  |  |  |  | GPIO02 | 
 | GPIO08 |  |  |  |  | 3v3 | DISPLAY – 3V3 –ROOD
 | GPIO11 |  |  |  |  | GND | DISPLAY – GND – ZWART
 | GPIO07 |  |  |  |  | GPIO14 | BEEPER – ROOD
 | GPIO06 |  |  |  |  | GPIO12 | 
ZWART – BEEPER | GND |  |  |  |  | GPIO13 | SCANNER – RX - GEEL
 | 3v3 |  |  |  |  | GPIO15 | SCANNER – TX - GROEN
 | EN |  |  |  |  | GPIO03 | BUTTON – SWITCH – GROEN
 | RST |  |  |  |  | GPIO01 | BUTTON – SWITCH – GROEN
VOEDING – GND | GND |  |  |  |  | GND | SCANNER – ZWART
VOEDING – 5v | Vin |  | USB |  |  | 3v3 | SCANNER – ROOD
GM60

## Slide 5
 | TOUT |  |  |  |  | GPIO16 | 
SCANNER – GND – GROEN | GND |  |  |  |  | GPIO05 | DISPLAY – SCL – BLAUW
SCANNER – 5V – ROOD | Vout USB |  |  |  |  | GPIO04 | DISPLAY – SDA – GROEN
Flash Data 3 pin | GPIO10 | ESP8266 |  |  |  | GPIO00 | BUTTON – SWITCH - GROEN
Flash Data 2 pin | GPIO09 |  |  |  |  | GPIO02 | BUTTON – SWITCH – GROEN
Flash Data 1 pin | GPIO08 |  |  |  |  | 3v3 | 
Flash CMD | GPIO11 |  |  |  |  | GND | PRINTER – GND – ZWART
Flash Data 0 pin | GPIO07 |  |  |  |  | GPIO14 | PRINTER – RX – GROEN
Flash CLK | GPIO06 |  |  |  |  | GPIO12 | PRINTER - TX – GEEL
Common LED’s / Buttons | GND |  |  |  |  | GPIO13 | BUTTON – LED - ROOD
 | 3v3 |  |  |  |  | GPIO15 | BUTTON – LED - ROOD
 | EN |  |  |  |  | GPIO03 | SCANNER – TX – ZWART
 | RST |  |  |  |  | GPIO01 | SCANNER – RX – GEEL
VOEDING – GND | GND |  |  |  |  | GND | DISPLAY – GND – ZWART
VOEDING – 5v | Vin |  | USB |  |  | 3v3 | DISPLAY – 3v3 - ROOD
GM67